## Slide 1: Chapter 4
  The Building Blocks: Binary Numbers, Boolean Logic, and Gates

## Slide 2: Learning Objectives (1 of 2)
Translate between base-ten and base-two numbers, and represent negative numbers using both sign-magnitude and two’s complement representations
Explain how fractional numbers, characters, sounds, and images are represented inside the computer
Build truth tables for Boolean expressions and determine when they are true or false
Describe the relationship between Boolean logic and electronic gates

## Slide 3: Learning Objectives (2 of 2)
Construct circuits using the sum-of-products circuit design algorithm, and analyze simple circuits to determine their truth tables
Explain how large, complex circuits, like 32-bit adder or compare-for-equality circuits, are constructed from simpler, 1-bit components
Describe the purpose and workings of multiplexer and decoder control circuits

## Slide 4: Introduction
This chapter introduces the fundamental building blocks of all computer systems
  Binary representation
  Boolean logic
  Gates
  Circuits
This chapter examines what the computing agent looks like and how it is able to execute instructions and produce results

## Slide 5: The Binary Numbering System (1 of 21)
How can an electronic (or magnetic) machine represent information?
Key requirements: clear, unambiguous, and reliable
External representation is human-oriented
  Base-10 numbers
  Keyboard characters
Internal representation is computer-oriented
  Base-2 numbers
  Base-2 codes for characters

## Slide 6: The Binary Numbering System (2 of 21)
Binary is the simple idea of On/Off, Yes/No, True/False, and Positive/Negative.
Binary is important to computing systems because of it’s stability and reliability.
  Even when an electrical system degrades, there is still a clear “On/Off.”
All data stored inside a computer is stored in binary (also called machine language) and interpreted to display on the screen in human language.

## Slide 7: The Binary Numbering System (3 of 21)

## Slide 8: The Binary Numbering System (4 of 21)
The binary numbering system is a base-2 positional numbering system
Base ten:
  Uses 10 digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, and 9
  Each place corresponds to a power of 10
  1,943 = (1 × 103) + (9 × 102) + (4 × 101) + (3 × 100)
Base two:
  Uses 2 digits: 0 and 1
  Each place corresponds to a power of 2
  1101 = (1 × 23) + (1 × 22) + (0 × 21) + (1 × 20) = 13

## Slide 9: The Binary Numbering System (5 of 21)
FIGURE 4.2 Binary-to-decimal conversion table
Binary | Decimal
0 | 0
1 | 1
10 | 2
11 | 3
100 | 4
101 | 5
110 | 6
111 | 7
1000 | 8
1001 | 9
1010 | 10
1011 | 11
1100 | 12
1101 | 13
1110 | 14
1111 | 15
Binary | Decimal
10000 | 16
10001 | 17
10010 | 18
10011 | 19
10100 | 20
10101 | 21
10110 | 22
10111 | 23
11000 | 24
11001 | 25
11010 | 26
11011 | 27
11100 | 28
11101 | 29
11110 | 30
11111 | 31

## Slide 10: The Binary Numbering System (6 of 21)
Converting from binary to decimal
  Add up powers of two where a 1 appears in the binary number
Converting from decimal to binary
  Repeatedly divide by two and record the remainder
  Example, convert 11:
    11 ÷ 2 = 5, remainder = 1, binary number = 1
    5 ÷ 2 = 2, remainder = 1, binary number = 11
    2 ÷ 2 = 1, remainder = 0, binary number = 011
    1 ÷ 2 = 0, remainder = 1, binary number = 1011

## Slide 11: The Binary Numbering System (7 of 21)
Computers use fixed-length binary numbers for integers, e.g., 4 bits could represent 0 to 15
Arithmetic overflow: when the computer tries to make a number that is too large, e.g., 14 + 2 with 4 bits
Binary addition: 0 + 0 = 0, 0 + 1 = 1, 1 + 0 = 1,
1 + 1 = 10 (that is, 0 with a carry of 1)
Example: 0101 + 0011 = 1000

## Slide 12: The Binary Numbering System (8 of 21)
Signed integers include negative numbers
Sign/magnitude notation uses 1 bit for the sign and the rest for the value
  +5 = 0101, -5 = 1101
  0 = 0000 and 1000!
Two’s complement representation: to make the negative of a number, flip every bit and add one
  +5 = 0101, -5 = 1010 + 1 = 1011
  0 = 0000, -0 = 1111 + 1 = 0000

## Slide 13: The Binary Numbering System (9 of 21)
Floating point numbers use binary scientific notation
  Scientific notation, base 10: 1.35 × 10-5
  Base 2: 3.2510 = 11.012 = 1.101 × 21
Characters and text: map characters onto binary numbers in a standard way
  ASCII (8-bit numbers for each character)
  Unicode (Minimum of 16-bit numbers for each character)

## Slide 14: The Binary Numbering System (10 of 21)
Sounds and images require converting naturally analog representations to digital representations
Sound waves characterized by:
  Amplitude: height of the wave at a moment in time
  Period: length of time until wave pattern repeats
  Frequency: number of cycles per unit time

## Slide 15: The Binary Numbering System (11 of 21)

## Slide 16: The Binary Numbering System (12 of 21)
Digitize: to convert to a digital form
Sampling: record sound wave values at fixed, discrete intervals
To reproduce sound, approximate using samples
Quality is determined by
  Sampling rate: number of samples per second
    More samples ► more accurate waveform
  Bit depth: number of bits per sample
    More bits ► more accurate amplitude

## Slide 17: The Binary Numbering System (13 of 21)

## Slide 18: The Binary Numbering System (14 of 21)
Image sampling: record color or intensity at fixed, discrete intervals in two dimensions
Pixels: individual recorded samples
RGB encoding scheme:
  Colors are combinations of red, green, and blue
  One byte each for red, green, and blue
Raster graphics store picture as two dimensional grid of pixel values

## Slide 19: The Binary Numbering System (15 of 21)

## Slide 20: The Binary Numbering System (16 of 21)

## Slide 21: The Binary Numbering System (17 of 21)
What is the space necessary to store the following data?
  1000 integer values
  10-page text paper
  60-second sound file
  480 by 640 image
Data compression: storing data in a reduced-size form to save space/time
  Lossless: data can be perfectly restored
  Lossy: data cannot be perfectly restored

## Slide 22: The Binary Numbering System (18 of 21)
Letter | 4-bit Encoding | Variable Length Encoding
A | 0000 | 00
I | 0001 | 10
H | 0010 | 010
W | 0011 | 110
E | 0100 | 0110
O | 0101 | 0111
M | 0110 | 11100
K | 0111 | 11101
U | 1000 | 11110
N | 1001 | 111110
P | 1010 | 1111110
L | 1011 | 1111111
 | (a) | (b)
Using variable-length code sets
Fixed Length
Variable Length

## Slide 23: The Binary Numbering System (19 of 21)
Computers use binary because “bistable” systems are reliable
  Current on/off
  Magnetic field left/right

## Slide 24: The Binary Numbering System (20 of 21)
Transistors
  Solid-state switches
  Change on/off when given power on control line
  Extremely small (billions per chip)
  Enable computers that work with gigabytes of data

## Slide 25: The Binary Numbering System (21 of 21)

## Slide 26: Boolean Logic and Gates (1 of 9)
Boolean logic is the rule for manipulating true/false expressions for binary machine language
Boolean expressions can be converted to circuits
Hardware design/logic design pertains to the design and construction of new circuits
Binary 1/0 maps to true/false of Boolean logic
Boolean expressions: x ≤ 35, a = 12
Boolean operators: (0 ≤ x) AND (x ≤ 35), (a = 12) OR (a = 13), NOT (a = 12)
  (0 ≤ x) • (x ≤ 35), (a = 12) + (a = 13), ~(a = 12)

## Slide 27: Boolean Logic and Gates (2 of 9)
Truth tables lay out true/false values for Boolean expressions, for each possible true/false input

## Slide 28: Boolean Logic and Gates (3 of 9)
FIGURE 4.14
Inputs: a | Inputs: b | Output a AND b (also written a . b)
False | False | False
False | True | False
True | False | False
True | True | True
Truth table for the AND operation

## Slide 29: Boolean Logic and Gates (4 of 9)
FIGURE 4.15
Inputs: a | Inputs: b | Output a OR b (also written a + b)
False | False | False
False | True | True
True | False | True
True | True | True
Truth table for the OR operation

## Slide 30: Boolean Logic and Gates (5 of 9)
FIGURE 4.16
Inputs: a | Output NOT a (also written ā)
False | True
True | False
Truth table for the NOT operation

## Slide 31: Boolean Logic and Gates (6 of 9)
Gate: an electronic device that operates on inputs to produce outputs
Each gate corresponds to a Boolean operator

## Slide 32: Boolean Logic and Gates (7 of 9)
Gates are built from transistors
NOT gate: 1 transistor
AND gate: 3 transistors
OR gate: 3 transistors
NAND and NOR: 2 transistors
Transistors can be in series or parallel

## Slide 33: Boolean Logic and Gates (8 of 9)

## Slide 34: Boolean Logic and Gates (9 of 9)

## Slide 35: Building Computer Circuits (1 of 18)
Circuit: has input wires, contains gates connected by wires, and has output wires
Outputs depend only on current inputs: no state

## Slide 36: Building Computer Circuits (2 of 18)
To convert a circuit to a Boolean expression
  Start with output and work backward
    Find next gate back, convert to Boolean operator
    Repeat for each input, filling in left and/or right side
To convert a Boolean expression to a circuit
  Similar approach
To build a circuit from desired outcomes
  Use standard circuit construction algorithm
    E.g., sum-of-products algorithm

## Slide 37: Building Computer Circuits (3 of 18)
Example from text
Build truth table

## Slide 38: Building Computer Circuits (4 of 18)
Example from text
Find true rows for Output-1

## Slide 39: Building Computer Circuits (5 of 18)

## Slide 40: Building Computer Circuits (6 of 18)

## Slide 41: Building Computer Circuits (7 of 18)
Compare-for-equality (CE) circuit
Input is two unsigned binary numbers.
Output is 1 if inputs are identical and 0 otherwise.
Start with 1-bit version (1-CE) and build general version from that.

## Slide 42: Building Computer Circuits (8 of 18)
1-CE circuit: compare two input bits for equality
Truth table
Boolean expression: (a • b) + (~a • ~b)

## Slide 43: Building Computer Circuits (9 of 18)

## Slide 44: Building Computer Circuits (10 of 18)
N-bit CE circuit
Input: a0a2…an-1 and b0b2…bn-1, where ai and bi are individual bits
Pair up corresponding bits: a0 with b0, a1 with b1, etc.
Run a 1-CE circuit on each pair
AND the results

## Slide 45: Building Computer Circuits (11 of 18)

## Slide 46: Building Computer Circuits (12 of 18)
Full adder circuit
Input is two unsigned N-bit numbers
Output is one unsigned N-bit number, the result of adding inputs together
Example
 |  |  |  | 1 | 
 | 0 | 0 | 1 | 0 | 1
+ | 0 | 1 | 0 | 0 | 1
 | 0 | 1 | 1 | 1 | 0
Start with 1-bit adder (1-ADD)

## Slide 47: Building Computer Circuits (13 of 18)

## Slide 48: Building Computer Circuits (14 of 18)
Sum digit, si, has the Boolean expression
  (~ai • ~bi • ci) + (~ai • bi • ~ci) +
  (ai • ~bi • ~ci) + (ai • bi • ci)
Carry digit, ci+1, has the Boolean expression
  (~ai • bi • ci) + (ai • ~bi • ci) +
  (ai • bi • ~ci) + (ai • bi • ci)

## Slide 49: Building Computer Circuits (15 of 18)

## Slide 50: Building Computer Circuits (16 of 18)

## Slide 51: Building Computer Circuits (17 of 18)
N-bit adder circuit
Input: a0a2…an-1 and b0b2…bn-1, where ai and bi are individual bits
a0 and b0 are least significant digits: ones place
Pair up corresponding bits: a0 with b0, a1 with b1, etc.
Run 1-ADD on a0 and b0, with fixed carry in c0 = 0
Feed carry out c1 to next 1-ADD and repeat

## Slide 52: Building Computer Circuits (18 of 18)

## Slide 53: Control Circuits (1 of 7)
Control circuits make decisions, determine order of operations, select data values
Multiplexer selects one from among many inputs
  2N input lines
  N selector lines
  1 output line
Each input line corresponds to a unique pattern on selector lines
That input value is passed to output

## Slide 54: Control Circuits (2 of 7)

## Slide 55: Control Circuits (3 of 7)
Decoder sends a signal out to only one output chosen by its input
  N input lines
  2N output lines
Each output line corresponds to a unique pattern on input lines
Only the chosen output line produces 1, all others output 0

## Slide 56: Control Circuits (4 of 7)

## Slide 57: Control Circuits (5 of 7)
Decoder circuit uses
  To select a single arithmetic instruction, given a code for that instruction
  Code activates one output line; that line activates corresponding arithmetic circuit
Multiplexer circuit uses
  To choose one data value from among a set, based on selector pattern
  Many data values flow into the multiplexer, only the selected one comes out

## Slide 58: Control Circuits (6 of 7)

## Slide 59: Control Circuits (7 of 7)

## Slide 60: Summary (1 of 2)
Computers use binary representations because they maximize reliability for electronic systems.
Many kinds of data may be represented at least in an approximate digital form using binary values.
Data can be compressed.
  Lossy: Some information is lost in the process.
  Lossless: No information is lost in the process.
Boolean logic describes how to build and manipulate expressions that are true/false.

## Slide 61: Summary (2 of 2)
We can build logic gates that act like Boolean operators using transistors
Circuits may be built from logic gates; circuits correspond to Boolean expressions
Sum-of-products is a circuit design algorithm: takes a specification and ends with a circuit
We can build circuits for basic algorithmic tasks
  Comparisons (compare-for-equality circuit)
  Arithmetic (adder circuit)
  Control (multiplexer and decoder circuits)